## Slide 1
DS3231 RTC
SD Card Writer
DATE TIME AND DATA LOGGING PRESENTATION

## Slide 2
The case for datalogging
Data without date time stamp is useless

## Slide 4
Storage Without Time Is Just Numbers in a File
At that point, you don’t really have data—you have detached values.
In practice:
Timestamp + value = information Value alone = noise

## Slide 5
In our previous example we learn how to:
Get Date – time information
Get Pico’s internal temperature
We now want these information data-logged for future reference
We can save the date/time information with the temperature values:
In Pico’s internal memory
In a SD Card
Cloud services such as Thingspeak
DB system such as InfluxDB
Problem with getting accurate Date/Time
Challenges in the field :
Source for Accurate Date/Time
Availability of Wi-fi/Internet

## Slide 6
Example_1.py
#connected to laptop
#no DS3231 real time clock module
#date time comes from the laptop

## Slide 7
Save the program as main.py
Unplug from laptop’s usb
Run from power bank
The date / time is now some unknown value
If you have wifi and internet connection, you can still get the correct
date time for the Pico W
- Using NTP

## Slide 8
What is NTP?
What NTP is
NTP = Network Time Protocol
It is a protocol used to get the accurate current time from servers on the internet.
It gives UTC time (Coordinated Universal Time)
Very accurate — usually within a few milliseconds to a second
Think of it as asking a “time server”:
“Hey, what time is it right now in UTC?”

## Slide 10
Example_2.py
#NOT connected to laptop
#no DS3231 real time clock module
#date time comes from the Internet

## Slide 12
This module converts the
Data we get from the ntpserver
Into human readable data
(2026,1,3,5,9,6,2,0)
year,month,day,weekday,hour,minute,second,subsecond)

## Slide 13
Example_3.py and setting_ds3231.py

## Slide 14
setting_ds3231.py – set the date time clock on the ds3231 Real Time Clock

## Slide 15
Setting_ds3231.py – sets the current time of the ds3231 RTC

## Slide 17
Once the current time is set, the ds3231 RTC will continue
To update itself with the current date/time like our watch.
A pico connected to it will get the RTC from it

## Slide 18
Example_3.py – Using the ds3231 with date that is already set.

## Slide 19
Then converted to human readable form
By these functions

## Slide 20
Then converted to human readable form
By these functions

## Slide 21
sd_card_demo.py
ssd1306 oled and ds3231
using the same i2c channel
ds3231 address = 0x68
We do not have to set date on the ds3231
Because we have set it earlier using
setting_ds3231.py

## Slide 22
Set up for SD Card Reader
It uses SPI comms
We want our program to create a csv file.
It has to be preceded with /sd/
“x” means we want to file to be created exclusively
If it is present, do not over-write it
f.write(“Date,Time,Temperature”)
Are column headers

## Slide 23
To human readable form