## Slide 1
LOCAL
AREA
NETWORK
WEB SERVER
192.168.0.1
WEB SERVER
192.168.0.2
WEB SERVER
192.168.0.3
WEBSOCKET HTTP REQUEST
For the controller to turn on the LEDs
Connect individually to the IP Address
Send the http Request
Cannot turn on the LEDs simultaneously
One to One Connectivity

## Slide 2
Device 1
Device 2
Device 3
MQTT - Message Queuing Telemetry Transport
For the controller to turn on the LEDs
Send the Message (Instruction to Broker)
Subscribers Receive the Message
Act on the Message Simultaneously
Allows Many to Many Connectivity
MQTT
BROKER
LAN
LAN
LAN

## Slide 3
HTTP PROTOCOL VS MQTT
This post office is the MQTT Broker

## Slide 4
Adafruit IO – MQTT Broker

## Slide 5
https://accounts.adafruit.com/users/sign_in
To use Adafruit MQTT Service
Create an Account

## Slide 6
Click Dashboards to Create Key
We need to create our unique API Key

## Slide 7
Click the Key Icon to Create

## Slide 8
Adafruit will assign
An Active Key
For your user name
Copy and save the Username and
Active Key somewhere because we
Will need them in our program later

## Slide 9
Next we will create the Feeds.

## Slide 10
Adafruit IO – MQTT BROKER
Username : soonseng
Temp
Pico1
28
ON
Feeds
Messages

## Slide 11
PUBLISHER
MESSAGE
FEED
MESSAGE
SUBSCRIBER
ON
ON
Username + feed = Topic
How MQTT works

## Slide 12
Creating a Feed in Adafruit IO

## Slide 13
Click on Feeds and then New Feed
Pico1
You will see the feed appearing here

## Slide 14
Create a Line Chart to display data

## Slide 16
Select the feed you are using
To send data to, then click next step

## Slide 18
Setting up the MQTT Connection to Broker (SUBSCRIBER)
Connect and Listen for Incoming Messages from Broker
Message is decoded from binary to string

## Slide 19
Setting up the MQTT Connection to Broker (PUBLISHER)
Connect and Publish Message to Broker
Temperature reading from the dht11.
Message must be converted to String
and encoded to binary/bytes

## Slide 20
MQTT – QUALITY OF MESSAGE DELIVERY
Adafaruit io does not support qos 2

## Slide 21
Download using the package manager
Click umqtt.simple and then click Install to Install Package
Installing the umqtt.simple package

## Slide 22
feed
MQTT DEMO
boiler_room.py
boiler_room_alarm.py

## Slide 23
Simulation of Boiler Room - Monitor
MQTT – Message Queue Telemetry Transport

## Slide 24
+
MQTT – Message Queue Telemetry Transport
Remote Boiler Room Alarm